FFT
Fast fourier transform:
A fast Fourier transform (FFT) is an algorithm that computes the discrete Fourier transform (DFT) of a sequence, or its inverse (IDFT).
An FFT rapidly computes such transformations by factorizing the DFT matrix into a product of sparse (mostly zero) factors.[2] As a result, it manages to reduce the complexity of computing the DFT from O(N^2), which arises if one simply applies the definition of DFT, O(N\log N), where N is the data size.
C-sim/Synthesis/Cosim
Original:
C-sim:

Synthesis:

the latency is unknown because there is an inner loop using the index of outer loop as its range. HLS can't estimate the accurate latency. So I decide to decrease the cycle period and do some optimization to make the FFT work even in a smaller period.
Cosim:

the original use the math cos and sin function which cost a lot.
So, I generate the cos and sin table by Octave.

Synthesis result

Not only the clk period is smaller, but also the utilization is 10 times smaller!!!
And then, I change the data type from float to fixed point. The utilization gets smaller!
I also write a simple function to replace the fabs function in math.h

Synthesis result

Hardware : AXI Master

Block design

Run on jupytor
I give the same input as the HLS one
and I write the result to a file and check if it's similiar to the HLS golden data
the result is what I expected.

golden data & output data:

github address:
https://github.com/guanhsu714/MSOC_self_paced/tree/master/Documents/MSOC/selfpaced