Cordic
Cordic:
Coordinate Rotation Digital Computer which is used to calculate trigonometric functions, hyperbolic functions, square roots, multiplications, divisions, and exponentials and logarithms with arbitrary base

C-sim/Synthesis/Cosim
Original:
C-sim:

Synthesis:

Cosim:

Float(change data type from fixed to float):
C-sim:

error is much lower than original.
Synthesis:

but latency and utilization are much larger as well because of the large computiation of floating points.
there's a trade off between utilization and precision, so i decided to increase the bits of the fixed point.
and I gave some tries on improvement.
#pragma HLS pipeline II=1
Synthesis:

apparently, the latency gets shorter.
then, I replaced the multipliers with shifters.
from

to

because shifters costs less resource than multipliers.

plus pipeline

and I increased the bit width of the data to get a better precision

though the utilization increases 2 times, the precision gets much better.

Hardware Implementation:
I used HLS Master as the interface

Run on jupytor
must use np.float32 as data type or it will be 8-bit float in default

github address:
https://github.com/guanhsu714/MSOC_self_paced/tree/master/Documents/MSOC/selfpaced