Squared Difference Accumulate
Squared Difference Accumulate:
Simply just input two values A and B, get A-B, and squre, and finally accumulate all the result.
C-sim/Synthesis/Cosim
Original:
C-sim:

Synthesis:

Cosim:

First, I add array partition and unroll on it. The factor = 2

In fact, the result is not that ideal. The utilization becomes two times larger, but the latency doesn't becomes two or more times smaller.
And then, I try to unroll more.
However, it gets worse.

Then, I try my best to lower the latency. I separate the "+=" which breaks the dependency and use an array to save the data first. Add them all in the end.

Result:

latency is 7 with no timing violations and a lot of utilization.
Then, I expand the unroll factor to 5.
latency is 6

Because the size of the array is 10, only the factor 10 in the factors bigger than 5 has the possibility to lower the latency.
However, it seems not good.
But the latency is down to 2.

Hardware : AXI Master

However, the output on the jupytor is only the answer for half process . I still can't figure it out.

github address:
https://github.com/guanhsu714/MSOC_self_paced/tree/master/Documents/MSOC/selfpaced