Histogram & Prefixsum
Prefixsum:
每個output就是除了加對應到的input之外，還要將前面的加起來
C-sim/Synthesis/Cosim
Original:
C-sim:

Synthesis:

Cosim:

First, I want to break the dependency between out[i] and out[i-1].
So that I can do more optimizations like unroll.

I use an integer to accumulate the value, so that every out[i] can be directly counted.
Then, I unroll the loop and do the array partition
Systhesis result:

Next, the necessary pipeline for the loop
Systhesis result:

I use the pipeline II=2 because there is a negative slack when II=1
As we can see, though the utilization is larger, latency is much smaller.
However, when I add the AXI interface to it, the timing has violations. I go to timing analysis and find out that the memory loading is critical path, so I guess doing array partition and pipeline at the same time will cause timing violations. As expected, when I disable one of them, the violations disappear.

Hardware : AXI Master

Run on jupytor:

Histogram:
就是將input當成output array的index，去計算到底各個value在input裡分別有幾個
C-sim/Synthesis/Cosim
Original:
C-sim:

Synthesis:

Cosim:

First, I just add pipeline II=1
But it can't be 1 because it is unable to enforce a carried dependence constraint between "store" operation on array "hist" and "load" operation on array "hist. So, II=2 in the end.
Synthesis:

We have to break the dependency

and we have to avoid storing and loading "hist" array at the same time.
However, there are timing violations.

it still needs time to store and load. In the end, I keep II = 2
Hardware : AXI Master

Run on jupytor

 github address:
https://github.com/guanhsu714/MSOC_self_paced/tree/master/Documents/MSOC/selfpaced